## Slide 1
Installation of Mainsailos on Raspberry 3b+ with raspberry imager, SD card needed.
->Other spec OS Mainsail 64 bit
Set wifi and password etc, host name is critical!
Configuring Multiple 3D Printers on Mainsail? Raspberry Pi x2 and Mainsail x2

## Slide 2
MainsailOS RP3b+ SKR2
Set wifi and password etc, host name critical!
Configuring Multiple 3D Printers on Mainsail? Raspberry Pi x2 and Mainsail x2

## Slide 3
cd klipper
make menuconfig
Make -> klipper.bin

## Slide 4
Rename Klipper.bin to firmware.bin and copy to SD card ->power on SKR2
Get firmware.cur if OK
Download FileZilla and connect to Raspberry 3b+

## Slide 5
FileZilla - Copy printer.cfg and upload to Mainsail

## Slide 6
Copy printer.cfg and upload to Mainsail

## Slide 7
lD USB
Tera Term = host=192.168.0.127-> pi1 and password
Get USB ID: ls /dev/serial/by-id/*
Release Tera Term 5.3 · TeraTermProject/teraterm

## Slide 8
Copy usb address to printer.cfg

## Slide 9
Enable TMC2209 in printer.cfg

## Slide 12
Volcano V6 Extruder Solution